## Slide 1
Midpoint Autonomous Tractor Presentation
Jai Deshmukh and Brendan Love
October 5, 2022

## Slide 2
01
Introduction

## Slide 3
The Project at a Glance
Real life Application: Use on Farms
Goal
  Save trip report w/ sensor and time data
  GUI for user control
  Cover the entirety of a scale field
Provided materials
  Tractor frame w/ 2 motors, 2 wheels, and swivel wheel
  L298N Motor Controller
  BLE Bluetooth module from DSD technology
  Ultrasonic distance sensor
  MPU9250 Gyroscope
  IR Emitter LED and IR receiver
Introduction
01
/

## Slide 4
Milestone One
Begin research for the project and outline a plan to stay on track for the rest of the project.
Week 3
Milestone Two
Implement most sensors to allow the tractor to drive forward and perform an emergency stop. Make the tractor drive in a straight path autonomously.
Week 6
Milestone Four
Design and implement a GUI to control the tractor and output data gathered through trip reports.
Week 12
Milestone Three
Begin interfacing with the tractor using the Bluetooth module. Implement the remaining IR sensor. Complete the autonomous path.
Week 9
Introduction
01
/
Milestone Overview

## Slide 5
02
Hardware Design

## Slide 6
Structural Design and Purpose
Platform for components that wouldn’t fit on the chassis
Raised to allow for easy access to the battery carriage
Wiring run underneath the platform in harnesses
Hardware Design
02
/

## Slide 7
Sensors
Sensor mount that fit in the existing cut outs for the infrared and ultrasonic sensors
Gyroscope and Bluetooth module mounted on the platform
Hardware Design
02
/

## Slide 8
03
Software Design

## Slide 9
Motor Control
L298N with PWM control for speed
IN1IN2’ = Left Forward
IN3’IN4 = Right Forward
PID loop to control individual motor speed
Software Design
03
/

## Slide 10
Gyroscope
Using MPU6050_light library
Gyroscope code first calculates offsets, then gets the following data every second (9600 bad):
Acceleration
Gyroscope
Magnetometer
Temperature
Data is used to make accurate turns and keep speed regulated in tractor.
Software Design
03
/

## Slide 11
Ultrasonic Sensor
Ultrasonic sensors get pulse duration
Calculates the distance in cm using the pulse time
Used to detect objects and prevent collisions
Software Design
03
/

## Slide 12
04
Reflections

## Slide 13: Issues Encountered and Solutions
TEAM | SECTION TITLE
The batteries were charged and tested. The team tested new pin assessments.
Current Draw Issue
The desired current to run the tractor is about 300mA from the battery carriage, however, only 50mA were measured.
I2C Communication Issue
The MPU9250 gyroscope would return special characters or wouldn’t return any data when being tested.
The team switched to the MPU6050 light library.
Problem
Problem
Solution
Solution
Reflections
04
/

## Slide 14
Planned Approach for the Future
IR Sensor Development
Week 8
Week 9
Week 10
Week 11
Week 12
Turning Implementation
Bluetooth Module Development
GUI Development
Final Adjustments
Reflections
04
/

## Slide 16
Questions?